## Slide 1: Digital Image Processing
ISE-2
Presented by:
Vaibhav Thombre (2015BCS025 )
Priya Mahajan (2016BTECS00206)
Guided by:
Dr. S. H. Bhandari

## Slide 2: Problem Statement
Automatic bottle filling inspection system using image processing.

## Slide 3: Algorithm
Take the color sample of liquid and convert it to HSV

## Slide 4: Set the lower And upper bounds of the Image
lower = np.array([hsv[0][0][0]-5, hsv[0][0][1]-50, hsv[0][0][2]-50])
upper = np.array([hsv[0][0][0]+5, hsv[0][0][1]+50, hsv[0][0][2]+50])

## Slide 5: Input image for checking the filled level Convert the image to HSV representation
img = cv2.imread(image_name)
img =
cv2.cvtColor(img, cv2.COLOR_BGR2HSV)

## Slide 6: Mask the bits for the pixels which are in predefined range
mask = cv2.inRange(img, lower, upper)

## Slide 7: Find the height of first few pixels from the top Find out amount of bottle filled
Assumption:
Standard height : 80 % of the height of the image
If bottle filled above 80 % consider it as full
else notified as empty bottle

## Slide 8: Results

## Slide 9: Level Detected on the image

## Slide 10
Thank You